## Slide 1
Digital Imaging in Pathology
- Past · Present · Future -
I will mention the names and products of many companies – I have no interests, financial or otherwise in any of them.
None of the material presented places me in a position involving conflict of interest.

## Slide 2
Digital Imaging in Pathology
- Past · Present · Future -

## Slide 3
Silver halide crystals form the basis of emulsion exposure photography
Silver halide crystals 0.2 - 2.0 microns
Resolution of crystals 6 - 10 microns
Grain (overlapping crystals) 10 - 30 microns (2540-847 dpi)
Human eye resolves 75 - 100 microns (340-254 dpi)
Photo sensor arrays:
Sensitive to light, do not discriminate color.
Two dimensional
Electrical connections must be made
(space between elements)
- Can be mechanically or electronically shuttered

## Slide 4
Focus image on chip ------- data moved ---------- stored in memory
Cameras for still photography
- hand held cameras
- on light microscope
- on electron microscope
Digital video recording
Primary storage
- in the camera
- on a computer
Secondary storage
- on a disc
- in USB flash drive
- on a network drive

## Slide 5
Acquisition ---- Display
Data has quantity and quality in both acquisition and display
Key points that drove development of electronic devices:
- Beyond your ability to perceive it, more dense data provides no visual advantage
- It is an advantage if you want to zoom or blow up an image
- The evolution of digital imaging centered on increasing resolution and color fidelity
- You can throw away excess data; there is a limit to improving poor data.

## Slide 6
Spectral response of the human eye

## Slide 7
Spectral response of a silicon photodiode

## Slide 9
Shuttering

## Slide 10
Adding Color
Filter wheel over monochrome chip
Prisms and 3 chips
Bayer mosaic filter over monochrome chip

## Slide 11
Foveon X3 Technology
“A Dramatically Different Design The revolutionary design of Foveon X3 direct image sensors features three layers of pixels. The layers are embedded in silicon to take advantage of the fact that red, green, and blue light penetrate silicon to different depths — forming the world's first direct image sensor”

## Slide 13
Foveon lacks color artifacts see with mosaic data.
Foveon gathers more light overall, but elements respond less crisply to color and lower layers do not collect as well.
Luminance is more difficult to measure with Foveon because blue is the wrong color to measure luminance. Bayer more accurately mimics human eye.
Foveon has more chromic noise.
Bayer has processing drain for interpolation, Foveon has processing drain to normalize the acquired data.
Foveolon Bayer

## Slide 14
Pixel size big vs small
Big = better light gathering Greater number of pixels, less
= more sensitive. sensitive.
In a comparison of a triple chip camera using 1.3 megapixel chips and a single 5 megapixel chip, the 1.3 megapixel chips produced a better image.

## Slide 15
Microlenses added for better light gathering

## Slide 16
Physical collection of interpixel data
Pixera Penguin
Ferromagnetic glass Lens + Magnets
Progres 3012
Zeiss Axiocam
Olympus DP 70 Lens

## Slide 17
Chip Cooling – Reduces Noise
Peltier Thermoelectric Device

## Slide 18
CMOS Sensors
Complimentary metal oxide silicon
CMOS Sensors:
Fundamentally different in construction and operation.
Made of same type of silicon as many solid state control devices so amplifiers, for example, can be formed on same silicon as sensors. Power consumption less, less heat, less noise.
X-Y addressing to acquire data directly, makes them fast.
CCD – off sensor processing CMOS – on sensor processing

## Slide 19
Train has arrived
- resolution and color fidelity has reached a point that the consumer will give up film.
- the benefits of being able to analyze, manipulate, and use the image surpasses film
in countless ways.
- image acquisition and sophisticated processing are now in the hands of the individual.
Kodak:
1975 – First digital camera 100x100 pixel 1988 – First megapixel camera
50MP 43.8 x 32.9mm CMOS sensor
Firewire 1995 Camera Link 2000 Gig E 2006 USB-3 2012

## Slide 20
Still shot quality reached level to replace film
High Quality Hand Held Cameras
large chips
change lenses
Photo Stand
cooled CCD
piezo shift or large chip
motorized Zoom Lens
Microscope Cameras
cooled CCD
piezo shift or large chip

## Slide 21
Developments after pixel shift
Fast transfer:
- Gig-E gigabit transfer over a network cable
- USB-3 (high speed USB, 5->10->20 Gbps)
(3.0, 3.1, 3.2 or 3.1 Gen1, 2,3)
Type A
Type B
USB 2 USB 3
RJ-45
Type A
B
USB-3 Micro-B
5 pin USB3
USB-2 USB2
Micro-B Mini-B
5 + 2
4 + 4

## Slide 22
Type A – plugs into computer or charger
USB 3 USB 2
Type B – plugs into peripheral device (printer, cell phone)
USB2 4 pin
USB3 7 pin
USB3 7 pin – with screw connector
usually supplied with camera
USB2 4 pin

## Slide 23
RJ-45
Ethernet Cables – Patch Cables – LAN Cables
not “crossed cable”
all have RJ-45 connectors , not part of specification.
First choice is:
Cat 5e 1 Gigabit to 100 meters 8 ft - $5.99 USD
Cat 6 3 Gigabit to 100 meters 8 ft - $8.99
Cat 6 10 Gigabit to 55 meters
Cat 6a 10 Gigabit to 100 meters 8 ft - $15.99
Cable options (Cat 6, 8 foot):
- Snagless Patch Cable $ 8.99
Shielded Patch Cable $11.99 Electromagnetic and Radio frequency interference (EMI/RFI)
Non-booted Patch Cable $ 8.99
Slim Patch Cable $10.99
Plenum Patch Cable $35.99 (7 ft) in air ducts, low smoke, low flame
TAA Snagless Patch Cable $10.99, 13.99 (7, 10 ft) TAA gov standard
Crossover Patch Cables - do not use -
10 colors
C2G.com , cablestogo.com

## Slide 24
1 2 3 4
1. Basler, acA1920-40uc 2.3 MP (1920x1200) 5.86 µ pixel 41 fps global shutter
2. Imaging Source, DFK 33GP5000e 5.3 MP (2592x2048) 4.8 µ pixel 22 fps global shutter
3. Dalsa, Genie TS-C4096 12.6 MP (4096x3072) 6.0 µ pixel 12 fps global shutter
4. Olympus DP72 1.36 MP (1360x1024) 6.45 µ pixel 15 fps progressive scan
3.2 MP (2070x15470 pixel shift
12.8 MP (4140x3096) pixel shift
2/3 in
6.6 x 8.8 mm
11 mm diagonal
1/1.2 in
7.1 x 11.3 mm
13.35 mm diagonal
1 in
9.6 x 12.8 mm
16 mm diagonal
n/a
18.43 x 24.57mm
31 mm diagonal
$525 CMOS $799 CMOS $6995 CMOS $8000 CCD pixel shift
DP74
1/1.2 in, 2.3 MP
5.86 µ pixel
60 fps
Fluorescence

## Slide 25
Sata Power Cable

## Slide 26
All are C-Mount, 25.4 mm opening
except
Dalsa Genie has a 42 mm opening
Olympus BX53
Stock couplers for:
0.35 x … 1/3 inch format
0.50 x … 1/2 inch format
0.63 x … 2/3 inch format
1.0 x … no optics

## Slide 28
Dove Tail Connection
Tube lens
Dove Tail

## Slide 29
Pointer, Filter
Tube Lens
Camera
coupler
Camera
Side Arm with Tube Lens
42 mm dovetail
46mm dovetail

## Slide 30
Edmund Optical:
C-mount 1 inch x 32
T-Mount M42 x 0.75
ThorLabs:
SM1 1.035 inch x 40
SM2 2.035 inch x 40
Dalsa Genie: M42 x1 (Pentax thread)
Thor has extensive line of thread adapters.
Thor has mounted lenses.
Edmund has more lenses of some types but you will have to mount them and accommodate their lens mount geometry.

## Slide 31
http://www.rafcamera.com
Company based in Belarus
Machine shop produces custom adapters (example: dove tail to C-mount) on demand in quantities of 1 or more.
Price $30 USD
Turn around:
Scale drawing for your approval (days).
Batches to anodize the machined tempered aluminum about 1 per week
Finished product within 2 weeks.
Mail, express from Belarus, 1-2 weeks.
Overall turn around, under 4 weeks.

## Slide 32
1 2 3
2/3 in
6.6 x 8.8 mm
11 mm diagonal
1/1.2 in
7.1 x 11.3 mm
13.35 mm diagonal
1 in
9.6 x 12.8 mm
16 mm diagonal
n/a
18.43 x 24.57mm
31 mm diagonal
$525 CMOS $799 CMOS $6995 CMOS $8000 CCD pixel shift
DP74
1/1.2 in, 2.3 MP
5.86 µ pixel
60 fps
Fluorescence
3
4
5
Aspect ratio 1:1.333
#2 f-100, 11.15 mm
#2 f-125, 8.95 mm, 80% of
available width, 64% of area.

## Slide 33
Performance:
Imaging Source 36 x 28 inch pixelate from 100% to 200% . 11.4 MB tiff . fov 890 microns /f125
Dalsa 56 x 42 inch pixelate from 100% to 200% . 36.9 MB tif . fov 880 microns /f250
Olympus 38 x 29 inch pixelate from 66.7% to 100 % . 38.1 MB tif . fov 712 microns /f ?
1. Basler, acA1920-40uc 2.3 MP (1920x1200) 5.86 µ pixel 41 fps global shutter
2. Imaging Source, DFK 33GP5000e 5.3 MP (2592x2048) 4.8 µ pixel 22 fps global shutter
3. Dalsa, Genie TS-C4096 12.6 MP (4096x3072) 6.0 µ pixel 12 fps global shutter
4. Olympus DP72 1.36 MP (1360x1024) 6.45 µ pixel 15 fps progressive scan
3.2 MP (2070x15470 pixel shift
12.8 MP (4140x3096) pixel shift

## Slide 34
1X
2X
3X

## Slide 35
Imaging Source: Microscope Camera (DFK MKU130-10x22)
DFK MKU130-10x22
Resolution: 4128 x 3096 (12.8 MP)
Shutter: Rolling
Frame rate: 30 fps @ < 1920 x 1080; 1 fps @ higher res.
Sensor : CMOS Exmor
Format: 1/2.5 (4.3 x 5.8 mm; 7.2 mm diagonal)
Pixels: 1.4 microns
Imaging Source 2592x2048 (1.42/4.82) = 8.5% Dalsa Genie 4096x3072 (1.42/62) = 5.4%
“Achieving and maintaining sharp focus in microscopy can be a challenging task. The Imaging Source 13 megapixel microscope camera has been designed to be a cost-effective, versatile solution for demanding microscopy applications. Featuring Sony CMOS technology, this camera comes equipped with a distortion-free autofocus lens which allows viewers to capture exactly what they see through the ocular rather than being limited to a region of interest. This camera can take the place of the ocular itself or can be screwed into the C-mount - eliminating the need for costly adapters. The camera's USB 3.0 interface makes a full HD preview (at 30 fps) on the host PC a reality”.

## Slide 36
Pixel improvements:
Exmor
6
1.4
7.2
16
31
4.8

## Slide 38
Whole Slide Imaging - WSI

## Slide 39
Load slide in above tray and insert in machine.
Machine previews slide and picks multiple focus points (or user may select the points).
Once machine is satisfied it begins scan and saves image to server.
Pathologist accesses server and examines image.
- Not all images scan well or at all (machine may reject).
- Telepathology is used as a backup (video camera
connected to a video server, accessible on high speed lan).

## Slide 41
Manual Scan with “Microvisioneer”
www.microvisioneer.com
Install was quick and easy
Drivers install with an executable.
Camera specified lists for $525.
Also need a USB-3 card and means to couple a C-mount camera to your microscope.
Software is $1989 for education and research, $2989 for commercial use.
Save as tif or svs, plenty of freeware viewers.

## Slide 42
VGA
Video In – Digital Out
Fast compression in hardware
Outputs:
- Composite video
- S-Video
- RGB Video

## Slide 43
Network Camera – Read Specs

## Slide 44
Gig-E
Compact package that can serve as a video and still shot camera
Robust sensors that compete with pixel shift
Imaging Source camera ships with easy to use software.
Dalsa software is very granular but at the developer and not user end.
Output on a network cable but not serving video or web media.
Exploring the possibility of remote viewing through VPN.
Streaming possible via software server.

## Slide 45
Define the mission – what do you need.
Consider those you serve, talk to them.
Discuss plans with others that have already deployed systems.
Get the computer services department involved. You will need someplace safe to store your images.
Be careful how you compromise, people grumble when you ask for more but quickly quiet when a new service runs well. They forget slowly when there is a big expenditure that produces a failed system.

## Slide 46
Hire an Informatics Professional
Stereotype

## Slide 47
Actual group of Informatics Professionals

## Slide 49
Mark Luquette, M.D.
LUQUE007@UMN.EDU
Lectures at IBDregistry.net
Charter Member of APIII,
Association for Pathology Informatics

## Slide 50
Tim Vitale, “Film grain, Resolution, and Fundamental Film Particles”, Version 20, April 2007, available at: http://cool.conservation-us.org/coolaic/sg/emg/library/pdf/vitale/2007-04-vitale-filmgrain_resolution.pdf
“Photochemical Photography” available at:
http://ffden-2.phys.uaf.edu/212_fall2003.web.dir/Mike_Kudenov%20/film.htm
“Photographic film” available at: https://en.wikipedia.org/wiki/Photographic_film
“Imaging Sensors That Capture Your Attention”, Sensors Magazine, Feb. 2001, available at:
http://www.siliconimaging.com/ARTICLES/sensors.htm
Nikon, Microscopy U, “Introduction to Charge-Coupled Devices” available at:
https://www.microscopyu.com/digital-imaging/introduction-to-charge-coupled-devices-ccds
Tiago Marques Godinho et al, “An efficient architecture to support digital pathology in standard medical imaging repositories”, Journal of Biomedical Informatics 71 (2017) 190–197.
Zoya Volynskaya, “Clinical Applications of Whole-slide Imaging in Anatomic Pathology”, Adv Anat Pathol 2017;24:215–221.
“Introduction to machine vision”, download at Cognex.com
Dean Faklis and G. Michael Morris, “Spectral properties of multiorder diffractive lenses”, Applied Optics @ vol. 34, no. 14,10 May 1995
Product literature at manufacturer’s websites: baslerweb.com, www.olympus-lifescience.com, teledynedalsa.com, theimagingsource.com